## Slide 1
Arduino Basics

## Slide 3
Development Board
Software AND hardware
Open source electronics platform
System to device communication

## Slide 4
Development Board
Software AND hardware
Open source electronics platform
System to device communication
Arduino Nano

## Slide 6
Arduino Nano
Arduino Nano

## Slide 7
Various types of Arduino
Arduino UNO
Arduino MEGA
Arduino NANO
Arduino LILYPAD

## Slide 8
Color coding of Resistors
25
102 ±5%
ohms

## Slide 10
HOW DOES IT COMMUNICATE WITH US?
Serial Communication

## Slide 12
Arduino uses 3 protocols for its communication
UART Communication Protocol
2. SPI Communication Protocol
3. I2C Communication Protocol

## Slide 13
UART- Universal Asynchronous Receiver Transmitter
1. UART is a form of serial communication because data is transmitted as sequential bits. The wiring involved with setting up UART communication is very simple: one line for transmitting data (TX) and one line for receiving data (RX). As you may expect, the TX line is used to for the data to send device, and the RX line is used to receive data.

## Slide 14
SPI- Serial Peripheral Interface
2. Devices communicating via SPI are in a master-slave relationship. The master is the controlling device (usually a microcontroller), while the slave (usually a sensor, display, or memory chip) takes instruction from the master.

## Slide 15
I2C- Inter Integrated Circuit
3. I2C addresses several drawbacks in the other communication protocols, giving it an advantage over the others in some applications. These include:
The ability to connect multiple masters to multiple slaves
Synchronicity (just like SPI), which means higher speed communication
Simplicity: implementation only requires two wires and some resistors

## Slide 18
Arduino IDE v1.8

## Slide 19
Compile/Verify
Upload to Board
New Sketch
Open .ino files
Save .ino files
Serial Monitor

## Slide 20
Serial Monitor

## Slide 21
VOID SETUP
VOID LOOP
Did anyone notice what were the two parts of the code ???

## Slide 22
Digital Input/Output
pinMode(pin, mode)
  Sets pin to either INPUT or OUTPUT
digitalRead(pin)
  Reads HIGH or LOW from a pin
digitalWrite(pin, value)
  Writes HIGH or LOW to a pin

## Slide 23
analogRead(pin)
Reads analog signal(value) from the pin and the ADC of the Arduino converts the value into digital format.
Analog Input

## Slide 25
Connect the USB Cable to the Arduino and your system

## Slide 26
How to resolve Port not showing in Arduino IDE
Try reconnecting your Arduino NANO to your system.
2. Try restarting the IDE.
3. If still the problem isn’t resolved yet, Don’t Panic! the driver must be missing and therefore Tech Support will install it in your system.

## Slide 27
Select the Port to which you connected your Arduino nano

## Slide 28
Select Processor as “ATmega328P (Old Bootloader)”

## Slide 29
Now Let’s do our first program!!
EXAMPLES
BLINK
BASICS

## Slide 31
void setup() {
pinMode(LED_BUILTIN, OUTPUT);
}
void loop() {
digitalWrite(LED_BUILTIN, HIGH);
delay(500);
digitalWrite(LED_BUILTIN, LOW);
delay(500);
}
The Code

## Slide 32
Upload your code

## Slide 33
LED Blinking using Arduino Minion

## Slide 34
BLINK

## Slide 35
Speakers : Astha Tiwari
Aditya Kamboj