## Slide 2: ANALOG TO DIGITAL CONVERTER (ADC)

## Slide 3: TYPES OF SIGNALS
ANALOG SIGNAL
DIGITAL SIGNAL
Notes: Telephone communica

## Slide 4: ANALOG SIGNAL
An analog signal is any continuous signal representing some other quantity, i.e., analogous to another quantity.
Notes: Analogous quantities like distance, sound, temperature, etc.

## Slide 5: DISCRETE SIGNAL
A discrete signal or discrete-time signal is a time series consisting of a sequence of quantities.

## Slide 6: DIGITAL SIGNAL
A digital signal is a signal that represents data as a sequence of discrete values; at any given time it can only take on, at most, one of a finite number(0,1)

## Slide 7: WHY IS AN ADC REQUIRED?

## Slide 8: ANALOG SIGNAL VS DIGITAL SIGNAL
(7)
(6)
(5)
(4)
(3)
(2)
(1)
(0)
Notes: Bits are least basic unit of information in communication.

## Slide 9: HOW DO WE CONVERT AN ANALOG SIGNAL TO DIGITAL SIGNAL?

## Slide 10
It has a three step process called SQE.
It includes: -
Sampling
Quantisation
Encoding

## Slide 11: SAMPLING
Sampling is a process of measuring the amplitude of a continuous-time signal at discrete instants, converting the continuous signal into a discrete signal.
The black lines towards the x-axis is a sample.

## Slide 12: TYPES OF SAMPLING
There are three types of Sampling: -
Under Sampling
Critical Sampling
Over Sampling.
Nyquist rate: - Fs ≥ 2Fm

## Slide 13: ACCURACY

## Slide 14: RESOLUTION

## Slide 15
Resolution of an ADC is how accurately it will sample (convert) the analog electronic signals into digital values (i.e. 0s and 1s).
Higher is the resolution then greater will be the accuracy.
No. of levels =2Resolution

## Slide 16: QUANTISATION

## Slide 17
Quantization is the process of mapping continuous amplitude (analog) signals into discrete amplitude (digital) signals. .

## Slide 18: ENCODING
Encoding is converting of discrete values to binary values.
8-bit encoder to 8-bits of binary digits

## Slide 19: ADC IN ARDUINO NANO
8 analog input pins
It has 10-bit ADC Will give digital value in the range of 0 – 1023
Function for analog input: analogRead()

## Slide 20: DIGITAL TO ANALOG CONVERTER

## Slide 21: PULSE WIDTH MODULATION(PWM)
PWM is a method of reducing the average power delivered by an electrical signal by getting it into discrete parts.
Notes: Transmitter to receiver
Modulation is process of changing the characteristics of carrier signal in accordance to message signal.

## Slide 22: PWM OUTPUT PINS IN ARDUINO NANO
6 PWM output pins.
Pin no. 3, 5, 6, 9, 10, 11
Denoted by a ‘ ~ ’
Syntax for analog output:
analogWrite()

## Slide 23: DUTY CYCLE
A duty cycle is the fraction of one period when a system or signal is active.
Duty Cycle =
TON
TON + TOFF
X 100%
Notes: Percentage of time the signal is active.

## Slide 25: PATTERN BLINKING USING ARDUINO NANO

## Slide 26: WHAT IS A BREADBOARD?

## Slide 28: JUMPER CABLES
MALE TO MALE
MALE TO FEMALE
FEMALE TO FEMALE

## Slide 29: CIRCUIT DIAGRAM

## Slide 30: CODE FOR PATTERN BLINKING
void setup()
{
pinMode(4, OUTPUT);
pinMode(5, OUTPUT);
pinMode(6, OUTPUT);
pinMode(7, OUTPUT);
}

## Slide 31
void loop() {
digitalWrite(4, HIGH);
delay(100); // Wait for 100 millisecond(s)
digitalWrite(5, HIGH);
delay(100); // Wait for 100 millisecond(s)
digitalWrite(6, HIGH);
delay(100); // Wait for 100 millisecond(s)
digitalWrite(7, HIGH);
delay(100); // Wait for 100 millisecond(s)

## Slide 32
digitalWrite(4, LOW);
delay(100); // Wait for 100 millisecond(s)
digitalWrite(5, LOW);
delay(100); // Wait for 100 millisecond(s)
digitalWrite(6, LOW);
delay(100); // Wait for 100 millisecond(s)
digitalWrite(7, LOW);
delay(100); // Wait for 100 millisecond(s)
}

## Slide 33: SPEAKERS: - ASHWIN KULKARNI SIDDHANT BHUSHAN