## Slide 2: ADXL345
Accelerometer for all​​

## Slide 3
What is an accelerometer?
It is an electromechanical device.
Measures proper acceleration along all 3 axes in the
3D coordinate plane.
Uses the principle of damped mass system.

## Slide 5
Types of accelerometers
Piezoelectric
Piezoresistive
MEMS

## Slide 6
PIEZOELECTRIC SENSOR
A material that has the ability to generate electric charge in itself on applying mechanical stress.
What is a piezoelectric material?

## Slide 8
PIEZORESISTIVE SENSOR
Change in electric resistivity of semiconductor or metal due to the application of mechanical strain.
What is piezoresistive effect?

## Slide 9
Many of you right now are like :
What exactly is a MEMS?

## Slide 10
MEMS
Micro-Electro-Mechanical Systems, or MEMS, is a technology that in its most general form can be defined as miniaturized mechanical and electro-mechanical elements (i.e., devices and structures) that are made using the techniques of microfabrication.

## Slide 12
3 axis accelerometer
A 3-axis accelerometer is a device that is designed to measure acceleration along three axes in space — the forward and back X-axis, the left and right Y-axis, and the up and down Z-axis.
The angle around each axis are respectively roll, pitch and yaw.

## Slide 13
I DON’T BELIEVE YOU,
SHOW ME A VIDEO

## Slide 14
A clear idea of these angles
Row pitch and yaw are rotational forces or moments along x,y, and z axes.
Roll happens in response to cornering centrifugal forces
Pitch happens in response to acceleration or deceleration
Yaw happens in response to cornering or side wind ; sharper the turn greater the yaw

## Slide 15
Let’s welcome our hero of the day…… ADXL345

## Slide 16
Ground
Common collector voltage
Chip select(Slave select)
Interrupt 1
Interrupt 2
Serial Data Out
Serial Data Line
Serial Clock Line
ADXL IC
Level Shifter IC
Voltage regulator IC

## Slide 23
Now let’s code!

## Slide 24
Including the library of Wire.h and why it’s used
#include <Wire.h>
#include <Adafruit_Sensor.h>
#include <Adafruit_ADXL345_U.h>
Adafruit_ADXL345_Unified accel = Adafruit_ADXL345_Unified();
float X_out, Y_out, Z_out; // Outputs
float roll, pitch, rollF, pitchF, yaw, yawF = 0;
int ADXL345 = 0x53;

## Slide 25
void setup(void)
{
Serial.begin(9600);
pinMode(2, OUTPUT);
pinMode(3, OUTPUT);
pinMode(4, OUTPUT);
Wire.begin(); // Initiate the Wire library
// Set ADXL345 in measuring mode

## Slide 26
Wire.beginTransmission(ADXL345); // Start communicating with the device
Wire.write(0x2D); // Access/ talk to POWER_CTL Register - 0x2D
// Enable measurement
Wire.write(8); // Bit D3 High for measuring enable (8dec -> 0000 1000 binary)
Wire.endTransmission();
delay(10);

## Slide 27
How to calibrate the offset of readings
//Off-set Calibration
//X-axis
Wire.beginTransmission(ADXL345);
Wire.write(0x1E);
Wire.write(1);
Wire.endTransmission();
delay(10);

## Slide 28
How to calibrate the offset of readings
//Y-axis
Wire.beginTransmission(ADXL345);
Wire.write(0x1F);
Wire.write(-2);
Wire.endTransmission();
delay(10);

## Slide 29
How to calibrate the offset of readings
//Z-axis
Wire.beginTransmission(ADXL345);
Wire.write(0x20);
Wire.write(-9);
Wire.endTransmission();
delay(10);

## Slide 31
Now back to Code
Now we will read the data from the accelerometer and print it on the serial monitor.
void loop(void)
{
sensors_event_t event;
accel.getEvent(&event);
X_out = event.acceleration.x;
Y_out = event.acceleration.y;
Z_out = event.acceleration.z;

## Slide 32
Now back to Code
Now we will read the data from the accelerometer and print it on the serial monitor.
Serial.print("X: "); Serial.print(event.acceleration.x); Serial.print(" ");
Serial.print("Y: "); Serial.print(event.acceleration.y); Serial.print(" ");
Serial.print("Z: "); Serial.print(event.acceleration.z); Serial.print(" ");
Serial.println("m/s^2 ");
delay(2000);

## Slide 33
This is how to calculate the values theoretically and below the code to calculate it by coding.
roll = atan(Y_out / sqrt(pow(X_out, 2) + pow(Z_out, 2))) * 180 / PI;
pitch = atan(-1 * X_out / sqrt(pow(Y_out, 2) + pow(Z_out, 2))) * 180 / PI;
yaw = atan(sqrt(pow(X_out, 2) + pow(Y_out, 2)) / Z_out) * 180 / PI;

## Slide 34
What are low-pass filter used for?
Low pass filters are used to filter noise from a circuit. 'Noise' is a high frequency signal. When passed through a low pass filter most of the noise is removed and a clear sound is produced. high-cut or treble cut filters.

## Slide 35
How to see the directions
Serial.print(rollF);
Serial.print("/");
Serial.println(pitchF);
Serial.print("/");
Serial.println(yawF);
float x = event.acceleration.x;
float y = event.acceleration.y;
float z = event.acceleration.z;
if ( x >= 8.5) {
digitalWrite(3, LOW);
digitalWrite(4, LOW);
digitalWrite(2, HIGH);
}
if (y >= 8.5) {
digitalWrite(2, LOW);
digitalWrite(4, LOW);
digitalWrite(3, HIGH);
}
if (z >= 8.5) {
digitalWrite(2, LOW);
digitalWrite(3, LOW);
digitalWrite(4, HIGH);
}
}

## Slide 37
Pin Connections
SDA – A4
SCL – A5
VCC – 5V
GND – GND
LED 1 - +ve end D2 –ve end GND
LED 2 - +ve end D3 –ve end GND
LED 3 - +ve end D4 –ve end GND

## Slide 43: Hope you learnt something new

## Slide 44: Ainesh and Parsh Signing off